## Slide 1: GLOSOLAN PT 2022: global outcomes and perspectives
Christian Hartmann
GLOSOLAN steering committee
IRD – France

## Slide 2
Context:
<<The mandate of the GSP is
to improve governance of the limited soil resources
of the planet
What you cannot (correctly) measure,
you cannot (correctly) manage.

## Slide 3
=> data provided by soil laboratories are essential for soil governance
(PHOTO WIKIPEDIA)
(PHOTO WIKIPEDIA)
Many data come from by soil laboratory analysis
Soil data can be obtained in different ways

## Slide 4
Soils are essential for food production:

## Slide 5
Laboratories are essential for soil data production
Soils are essential for food production:
Soil labs:
where soil data begins

## Slide 6
Soils are essential for food production:
The good news : soil labs already exist all around the planet
Soil labs:
where soil data begins
Laboratories are essential for soil data production

## Slide 7
Soils are essential for food production:
The good news : soil labs already exist all around the planet
The bad news: soil labs are working without coordination among them…
Soil labs:
where soil data begins
Laboratories are essential for soil data production

## Slide 8
Soils are essential for food production:
Soil labs:
where soil data begins
The good news : soil labs already exist all around the planet
The bad news: soil labs are working without coordination among them…
An option for improvement:
Laboratories are essential for soil data production

## Slide 10
The 900 labs that are GLOSOLAN members 

## Slide 11
For 5 years now GLOSOLAN helped these labs producing reliable and comparable soil data
by providig SOPs, video explaining SOPs, trainings, webinars, technical publications, etc…
The 900 labs that are GLOSOLAN members 

## Slide 12
Now GLOSOLAN questions are:
1. How reliable and comparable are the data produced by soil laboratories?
2. How can GLOSOLAN help all labs to reach a minimum data quality?
For 5 years, GLOSOLAN has been helping soil labs producing reliable and comparable soil data
by providing SOPs, video explaining SOPs, trainings, webinars, technical publications, etc…

## Slide 13
Part 1 = assessment:
how reliable and comparable are
the data produced by soil laboratories?

## Slide 14
Launching a global (planet) proficiency testing (PT)
or inter-laboratory comparison.
The PT design was decided according to:
our QUESTIONS (reliability / comparability)
& FEASABILITY
(number of soil types, cost of preparation including irradiation,
cost of sending worlwide, etc)

## Slide 15
QUESTIONS: 2 + 1 more
RELIABILITY: for each lab, what is its precision?
(i.e. when analysing several times the same sample,
how close are the results?)
2. COMPARABILITY: among all labs, dispersion of their results?
(i.e. when the same sample is analysed by several labs,
how close are the results?)
3.

## Slide 16
QUESTIONS: 2 + 1 more
RELIABILITY: for each lab, what is its precision?
(i.e. when analysing several times the same sample,
how close are the results?)
2. COMPARABILITY: among all labs, dispersion of their results?
(i.e. when the same sample is analysed by several labs,
how close are the results?)
3. REFERENCE VALUE : at global scale, consensus value = reference value?
(i.e. on a statistical and practical view point,
can we provide samples with reference values acceptable worldwide?)

## Slide 17
FEASABILITY:
Which soil characteristics?
2. How many replicates?
3. Which range?

## Slide 18
FEASABILITY:
Which soil characteristics?
pH: top priority but difficult because to much soil weight is needed

## Slide 19
FEASABILITY:
Which soil characteristics?
pH: top priority but difficult because to much soil weight is needed
C: top priority because
- soil is a main compartment in C cycle… global warming…
- and…

## Slide 20
List of contributors:

## Slide 21
List of contributors:

## Slide 22
FEASABILITY:
Which soil characteristics?
pH: top priority but difficult because to much soil is needed…
C: top priority because
- soil is a main compartment in C cycle
- and « Protocole of assessment of sustainable management »
- low soil amount is needed
N & P: main factors of productivity / negative impact on environment
low soil amount is needed

## Slide 23
FEASABILITY:
Which soil characteristics?
pH: top priority but difficult because to much soil weight is needed
C: top priority because
- soil is a main compartment in C cycle
- and « Protocole of assessment of sustainable management »
- low soil amount is needed
N & P: main factors of productivity / negative impact on environment
low soil amount is needed
Which methods?

## Slide 24
Carbon
≠ METHODS
Walckley & Black
Dumas
Loss of ignition
≠ TOOLS
Wet chemistry
Combustion (controled atmosphere)
Combustion (450-550°C)

## Slide 25
Carbon
Walckley & Black
Dumas
Loss of ignition
Wet chemistry
Combustion (controled atmosphere)
Combustion (450-550°C)
For some methods,
≠ procedures are possible
≠ METHODS
≠ TOOLS
Temperature
NA
duration

## Slide 26
Nitrogen
Soil characteristic
Kjeldahl
Wet chemistry
Combustion (controled atmosphere)
For some methods,
≠ procedures are possible
Dumas
≠ METHODS
≠ TOOLS

## Slide 27
Phosphorus
Olsen
Bray 1
Bray 2
0.5 M NaHCO3 solution,
adjusted at a pH of 8.5.
0.03 M NH4F and 0.025 M HCl
0.03 M NH4F + 0.1 M HCl
For some methods,
≠ procedures are possible
≠ METHODS
≠ EXTRACTANTS
shaking times

## Slide 28
FEASABILITY:
Which soil characteristics? C N P
2. How many replicates?

## Slide 29
2. How many replicates?
Enough rep. to be able to make a statistical analysis,
Not to much to avoid reduced efficiency
6 rep:
A B C D E F
Comparability
Reliability
Compare all labs
of each individual lab

## Slide 30
2. How many replicates?
Enough rep. to be able to make a statistical analysis,
Not to much to avoid reduced efficiency
6 rep:
A B C D E F
Comparability
Reliability
Compare all labs
of each individual lab
Estimated through PRECISION
Is the analytical process under control?
or is random

## Slide 31
WHY PRECISION IS IMPORTANT:
If you go up and down your balance,
you expect the same result everytime

## Slide 32
If you make several times the test (within short time)
You expect the same result
WHY PRECISION IS IMPORTANT:

## Slide 33
(comment:
relevant, whatever the method and procedures used by the labs)
5 times the same result?
5 REPLICATES

## Slide 34
FEASABILITY:
Which soil characteristics? C N P
2. How many replicates? 6 soil types & 5 rep for one soil

## Slide 35
FEASABILITY:
Which soil characteristics? C N P
2. How many replicates? 6 soil types & 5 rep
3. Which range?

## Slide 36
FEASABILITY:
Which soil characteristics? C N P
2. How many replicates? 6 soil types & 5 rep
3. Which range?
LOW to HIGH carbon content

## Slide 37
FEASABILITY:
Which soil characteristics? C N P
2. How many replicates? 6 soil types & 5 rep
3. Which range?
LOW to HIGH carbon content
0.2 to 6 % carbon

## Slide 38
FEASABILITY:
Which soil characteristics? C N P
2. How many replicates? 6 soil types & 5 rep
3. Which range? 0.2 to 6 % carbon
A B C D E F
E
E
E
E
10 SOIL SAMPLES

## Slide 39
After you sent the analysis , still a lot of work was done
Make the statistical analyse and check
Processes with customs for ‘difficult’ countries
Contact the labs that were late
Contact the labs that did not follow the recommandations (no C data…)
Individual lab performances
Regional performances
etc…

## Slide 40
GLOBAL RESULTS

## Slide 41
Statistical procedure
----
Consensus values

## Slide 48
Precision

## Slide 49
Precision: interpretation of Z-score standard deviation (sd)

## Slide 50
Carbon

## Slide 51
0.4
0.8
1.2
Standard deviation
(sd)

## Slide 53
OK
the analytical process
is under control

## Slide 54
OK
Half have
problems

## Slide 55
OK
Half have
problems
Some have very
serious problems

## Slide 56
OK
Half have
problems
Analytical problems or transcription problems?
Anyway clients gets low quality
and unreliable data

## Slide 58
Using high tech. instruments but still problems => human factor?

## Slide 59
Majority is OK but unreliable method

## Slide 60
Nitrogen

## Slide 62
> half have
problems
Many have very
serious problems

## Slide 64
Using high tech. instruments but still problems => human factor?

## Slide 65
Phosphorus

## Slide 67
A majority is OK ! 
Few labs still had serious problems

## Slide 69
A large majority is OK !  
Marginal
problems

## Slide 70
Nearly all labs are OK !  

## Slide 72
Comparability
& accuracy
How distant/different are the results from each lab
Compared to the consensus value.

## Slide 73
Carbon

## Slide 75
Average of the 10 Z score for the 10 analyses made
Possible to calculate a standard deviation:
+ short error bar: similar performances for all 10 samples (even the 2 extreme values)
+ long error bar: different performances

## Slide 76
By chance some labs have an good average performance but indeed the performances different (very different) between samples
=> It was useful to have a large range of content
Whatever the difficulty of the method, some labs made it very well for a large range of C content.

## Slide 77
Technology cannot solve all problems!
The human factor is important too

## Slide 80
Nitrogen

## Slide 81
High perf.
Low perf.
Medium perf.
Low perf.

## Slide 82
The human factor ?

## Slide 84
Phosphorus

## Slide 90
Part 1 = assessment:
how reliable and comparable are
the data produced by soil laboratories?

## Slide 91
QUESTIONS: 2 + 1 more
RELIABILITY: for each lab, what is its precision?
many labs have insuficient precision: need to develop IQC

## Slide 92
QUESTIONS: 2 + 1 more
RELIABILITY: for each lab, what is its precision?
many labs have insuficient precision: need to develop IQC
2. COMPARABILITY: among all labs, dispersion of their results?
Depends on method but even with high tech
Analytical problems &/or transcription mistakes ?

## Slide 93
QUESTIONS: 2 + 1 more
RELIABILITY: for each lab, what is its precision?
many labs have insuficient precision: need to develop IQC
2. COMPARABILITY: among all labs, dispersion of their results?
Depends on method but even with high tech
Analytical problems &/or transcription mistakes ?
3. REFERENCE VALUE : at global scale,
consensus value = reference value : YES !

## Slide 94
Done but need to go forward

## Slide 95
Done but need to go forward
Record of performances but not yet certificates

## Slide 96
Part 2 = future perspectives:
(suggestions to be discussed)
Which actions/activities
to improve all labs performances ?
- Organisation of regional PTs in 2023

## Slide 97
let’s consider the laboratories as ‘factories producing data’
global situation of labs was a black box
GLOSOLAN has opend the dor and brought some light…
preparation
Analytical process 1
Analytical process 2
Analytical process 3
Analytical process 4
Analytical process etc
registration
storage
client
Keep the duration as short as possible
Report
(results, data)
Soil lab
= black box
client
SOIL

## Slide 98
preparation
pH
Carbon
Nitrogen
Phosphorus
Texture
registration
storage
client
SOIL
Report
(results, data)
client
CEC
Etc…
This is how it looks inside the ‘factory’:

## Slide 99
preparation
Carbon
Nitrogen
Phosphorus
registration
storage
client
SOIL
Report
(results, data)
client
This is how it looks inside the ‘factory’:
This is what we have tested with GLOSOLAN PT
What did we discover & what can be proposed?

## Slide 100
preparation
Carbon
Nitrogen
Phosphorus
registration
storage
client
SOIL
Report
(results, data)
client
This is how it looks inside the ‘factory’:
LACK OF INTERNAL QUALITY CONTROL
For the analytical processes ?
For the transcription/ secretary processes ?

## Slide 101
preparation
Carbon
Nitrogen
Phosphorus
registration
storage
client
SOIL
Report
(results, data)
client
This is how it looks inside the ‘factory’:
LACK OF INTERNAL QUALITY CONTROL
For the analytical processes ?
For the transcription/ secretary processes ?
Labs with poor ‘precision’ performances need to take action
Request GLOSOLAN members support or GSP/GLOSOLAN secretary
(confidentiality garanteed!)

## Slide 102
EXTERNAL QUALITY CONTROL?
ABSOLUTELY NECESSARY BUT…
Cannot be organised by GLOSOLAN for all labs
REGIONAL PTs are necessary

## Slide 103
EXTERNAL QUALITY CONTROL?

## Slide 104
EXTERNAL QUALITY CONTROL?
ABSOLUTELY NECESSARY BUT…
Cannot be organised by GLOSOLAN for all labs

## Slide 105
EXTERNAL QUALITY CONTROL?
ABSOLUTELY NECESSARY BUT…
Cannot be organised by GLOSOLAN for all labs
REGIONAL PTs are necessary… how to do?

## Slide 106
REGIONAL PTs are necessary… how to do?
Each region or sub-region must organise PTs
Glosolan will organise GLOBAL PTs involving only high performing labs to assure accuracy and comparability

## Slide 107
Human factor ?

## Slide 108
Human factor ?
GLOSOLAN has done many activities to help labs
Now GLOSOLAN needs the help of high performing labs to train the less successful labs,
on a regular basis…

## Slide 109
Human factor ?
GLOSOLAN has done many activities to help labs
Now GLOSOLAN needs the help of high performing labs to train the less successful labs,
on a regular basis…
All participants know where they are..
Performances

## Slide 110
Human factor ?
GLOSOLAN has done many activities to help labs
Now GLOSOLAN needs the help of high performing labs to train the less successful labs,
on a regular basis…
All participants know where they are..
Performances

## Slide 111
It is important to reach the highest step….
It is also important to help each other to reach
the highest step!

## Slide 112
Human factor ?
GLOSOLAN has done many activities to help labs
Now GLOSOLAN needs the help of high performing labs to train the less successful labs,
on a regular basis…
All participants know where they are..
FOR THE FUTURE
Performances

## Slide 113
Precision
Accuracy
Health &
Safety too !
Data are important
People &
environment

## Slide 114
Precision
Accuracy
Health &
Safety too !
Data are important
People &
environment
On going, should develop…

## Slide 115
Record of performances but not yet certificates

## Slide 116: Thank you also to Lucrezia, Nok, Michael, Filippo, and many others who all joined the work that I presented. Without their dedication GLOSOLAN would not have such an unique vision of GLOBAL soil labs!
Thanks for your attention Thank you to PT participants